Instruction lines will be 16 bits long - > 1 byte for instruction, 1 byte for instruction data.

00 000 000 0000 0000

The two first bits are to specify the kind of instruction that the CPU have to execute. From bit 3th to 8th of the instruction byte, is the instruction body and its structure will depends on the actual instruction. The data byte will be use to move, store, and insert those values. It can represent either data --on numbers or characters--, pointers to memory, or instructions.
Each kind of instruction will have a different structure; but, the standard form is 2 bits for instruction, 3 for reg, and 3 for parameter, the other byte is for data used in the instruction line

Arithmetic:
 There is a specific register used as “output” of the operation. You can move “from”, but not “to” it.

Syntax:

00 00 000 0 0 0 000 000

00 >> Instruction: Arithmetic
00 >> Operation type
0000 >> Options
0 >> Neg input B
000 >> Reg input B
0 >> Neg input A
000 >> Reg input A

There is 4 operation types:
Add Operation: 00 →
Using a full adder, you can add the two inputs regs. There is one output: the result, and three flags: ZERO, NEGATIVE, and OVERFLOW. As the adding operation doesn’t have more options, three of the four bits using for options, will be used as direction of output reg. If you want to use the default ALU output reg, you just have to True the last instruction bit.

00 00 000 0 0 0 000 000

Example:
- 00 00 010 0 0 110 0 010 = Arithmetic/add: store, on register 2, the value of register 6 plus the value on register 2.
- 00 00 001 0 1 011 0 100 = Arithmetic/add: store, on register 1, the negative value of register 3 plus the value on register 4.
- 00 00 000 1 0 000 0 101 = Arithmetic/add: store, on default, the value on input plus the value on register 5.
- 00 00 000 0 1 111 1 000 = Arithmetic/add: store, on output, the negative value on register 7 plus the negative value on of input.
- Logic operation: 01 →
You can chose the specific operation with the Options bits. The result will be store on the	ALU output reg. There is a bit to negate the output; if this bit is used on 111, then will give as result input B.
00 01 000 00 0 000 000
Operations:
00 >> OR
01 >> AND
10 >> XOR
00 >> NOT

Example:
- 00 01 000 0 0 110 1 000 = Arithmetic/logic: OR value on reg 6 and negative value on input.
- 00 01 101 0 0 001 0 111 = Arithmetic/logic: NOT value on reg 1.
- 00 01 100 1 1 000 1 101 = Arithmetic/logic: OR and negate the negative value on input and negative value on reg 5.
- 00 01 111 0 0 000 0 000 = Value on input.

Shift Operation: 10 →
In the shifting operation you can choose which operation you want to execute by using the	5th and 6th bits. The data information is used as direction of the input register and output	register; also, you have an extra bit in each register to neg the values.

00 10 000 0 0 0 000 000

Operations:
0 >> Shift Left
1 >> Shift Right
Examples:
- 00 10 000 0 1 101 0 000 = Arithmetic/shifting: logic shift to the left of neg value on reg 5 into output.
- 00 10 111 1 0 000 1 101 = Arithmetic/shifting: just rotate, rotate value on input into reg 5 and negate it.
- 00 10 011 1 1 110 0 110 = Arithmetic/shifting: arithmetic shift to the right the negative value in reg

Condition Operation: 11 →