Basic Syntax

The arithmetic in the CalOX’s CPU will be executed as combinational circuit and all in the same ALU. There will be 2 inputs (A and B), and one output. The bool operations doesn’t have a specific output, it works by jumping to a location of memory if the statement result was true.
The last 6 bits of the instruction line are use to specify the inputs regs, 3 bits for A value and 3 for B value. 5th - 7th bits are use as return value, you have to put the register number in where you want to store the result. 8Th - 10th are used as operation parameters. Each operation will have different parameters like negate the inputs in addition, or NOT the output in Logic OP.
The Shifting operation will have only 1 input (last 3 bits). The 3 digits before are use as shifting amount.
The syntax will be not the same for all operation, but we can simplify it like this:

Syntax:

00 00 000 0 0 0 000 000

00 >> Instruction: Arithmetic
00 >> Operation type
000 >> Return reg
0 0 0 >> Parameters
000 >> A value
000 >> B value

Parameters will be the main different between each operation type.

Operations

There is 4 operation types: Add Op, Logic Op, Shifting Op, and Bool Jumps. Each type of operation have its own syntax, but all of them have main similarities.
Add Operation: 00
Using a full adder, you can add the two inputs regs. There is one output: the result, and three flags: ZERO, NEGATIVE, and OVERFLOW. With the parameters you can negate the return value, and the A and B values.

00 00 000 0 0 0 000 000
00 >> Arithmetic
00 >> Addition Op (00)
000 >> Return register
0 >> Negate return value
0 >> Negate A
0 >> Negate B
000 >> A value
000 >> B value

### Examples:
Logic operation: 01
There are four different logic operations, you can choose it using the 2 first parameters bits. The extra parameter bit is used to NOT the return value. This is the same for all the operations excepts for NOT operation. When you use NOT, then the extra bit is used to choose between return the NOT of A if 0 and the NOT of B if 1.

Operations:
00 >> OR
01 >> AND
10 >> XOR
11 >> NOT
00 00 000 00 0 000 000

00 >> Arithmetic
00 >> Logic Op (01)
000 >> Return register
00 >> Operation
0 >> NOT return value / choose between NOT A or NOT B as return
000 >> A value
000 >> B value

### Examples:

Shifting Operation: 10
In the shifting operation you can only use one value. There first parameter ask if you want to rotate; if you choose rotate, then the other parameters will be used to NOT and negate the return value. If you didn’t rotate, the second parameter is for choosing the sifting direction (0 for left), and 3th make an arithmetic shift. 11Th - 13th bits is the shifting amount, doesn’t do anything with rotation.

00 00 000 0 0 0 000 000

- 00 >> Arithmetic
- 00 >> Shifting Op (10)
- 000 >> Return register
- 0 >> Rotate
- 0 >> Shift direction (0 for left) / NOT return value
- 0 >> Arithmetic Shift / Negate return value
- 000 >> Shift amount
- 000 >> A value
### Examples:

Bool Jump: 11
The bool jump operation works partially different than other operation. This one will not give a return value; instead, it will substitute the actual CPU counter value to allow code jumps. 5Th - 7th bits are use as a reference to the reg with the value you want to put into the counter. True the first parameter bit if you want to compare A value with 0 (Negative, Positive, Zero), or False it if you want to compare an A value with a B value (Less than, More than, Equal to). There is an option to True always.

Operations:
00 >> Iqual to 0 / B
01 >> Less than 0 / B
10 >> More than 0 / B
11 >> True Always

00 00 000 0 00 000 000
- 00 >> Arithmetic
- 00 >> Bool Jump (11)
- 000 >> Reg with memory direction
- 0 >> Compare with B
- 00 >> Operations
- 000 >> A value
- 000 >> B value
### Examples: